## Slide 1: LM-470 REMOVAL & INSTALLATION
The LM-470 is a 72 foot tower that weighs about 1100 pounds. To move the tower requires a long trailer and a ¾ ton truck with towing capabilities. The tower was in Valley Springs and was moved to Wilton, CA. Then comes the fun.

## Slide 2: The sled is designed to hold the bottom of the tower and allow clearance for the drum and cables. Eye bolts allow the sled to be dragged into position.

## Slide 3: Tilt trailer is driven into position at the base of the tower. Trailer is 20 feet long.

## Slide 4: A 4 inch pulley is installed 7 and a half feet up the tower. Starting down.

## Slide 5: The trailer tilts when the weight of the tower is applied.

## Slide 6: The antenna is fully down and parallel with the bed.

## Slide 7: A dolly and some 4X6s support the top of the tower.

## Slide 8: A pair of come alongs are used to center the tower and pull the sled into position.

## Slide 9: Dolly removed.

## Slide 10: Sled is in position and ready for final tie down. Time on site was 2 hours.

## Slide 11: Once in the back pasture in Wilton, the Bob Cat fork lift easily handled the load.

## Slide 12: The sled and other lumber were used to safely support the tower until the base is ready.

## Slide 13: The rebar cage arrives. We rolled the cage off the tailgate.

## Slide 14: #10 rebar is welded to the mounting ears. The tops of the rebar were ground flat so the frame could be leveled.

## Slide 15: The ears are attached to the base of the tower.

## Slide 16: Support rebar is welded to the #10 bars before it is removed. The all-thread and steel braces hold the position of the rebar. This was a necessity as the base frame was bounced around but never lost its shape or alignment.

## Slide 17: The support 2X4 lumber is added. One stud for each rod with a hole to give ½ inch space above the cement level so the cement would flow between the sides.

## Slide 18: Excavator arrives

## Slide 19: Target

## Slide 20: Painting the ground

## Slide 21: Precision scraping

## Slide 22: Hardpan

## Slide 23: Squaring the hole

## Slide 24: Gopher

## Slide 25: Hog wire was added to stabilize the sides. Measuring post was marked for depth of hole and the level of crushed rock.

## Slide 26: Dropping in the cage

## Slide 27: Ready for cement. Galvanizing painted to the rebar and ears. Foundation stakes hold the form level. The “T” braces are to hold the shape without making the sides unstable.

## Slide 28: The footings and rebar needed adjustment. How did he get in and how did he get out?

## Slide 29: Adjusting blocks that are ½ inch thick are under each end of the studs to bring the frame to the correct level. Small blocks were installed to keep the frame from moving. Two door shims were needed to make the base frame level.

## Slide 30: Cement truck arrives

## Slide 31: Trying to be neat

## Slide 32: Filling in the holes.

## Slide 33: Starting the leveling and the filling of some counter weights.

## Slide 34: Cement workers

## Slide 35: Getting it flat

## Slide 36: Still level. It never moved but we could have adjusted it if we needed to.

## Slide 37: After a week, the forms were removed, the remainder of the steel was galvanized and the tilt frame installed. The XR-5 and other antennas were assembled.

## Slide 38: Dollies are placed under the sled and the tower top. Scrap plywood is placed on the ground and the tower pushed towards the base.

## Slide 39: Tower lined up with the base.

## Slide 40: Dolly and sled must be removed, so a floor jack takes and lowers the load. The lifting winch holds the tower in place.

## Slide 41: First 2 bolts are in.

## Slide 42: The motor and drum will hit the ground, so a small hole is dug to protect the winch.

## Slide 43: Rigging the pulleys

## Slide 44: Coming up

## Slide 45: All the bolts were inserted to make sure they all would fit. A large pry bar was needed for the rear holes.

## Slide 46: Tilting the tower backward

## Slide 47: Chain is attached to the counter weight.

## Slide 48: Weight makes the cranking easier.

## Slide 49: Mast and rotor are added. The cement block weighs about 250 pounds.

## Slide 50: Mast comes close enough to the ground for easy attachment of the upper antennas.

## Slide 51: Tower is pulled vertical so the rotor can be centered and tested.

## Slide 52: The XR-5 is on the bottom, the 40 meter dipole is in the middle and the 4 element yagi for 6 meters is on the top.